## Slide 1: 3D Printer and Application Interface Cody Hutchison Steven Liu Abigail Morar

## Slide 2: Executive Summary
Problem Statement
  Current 3D printers require the user to manually upload a G-code file by an external storage device and initiate the printing process via controls on the printer
Solution
  The new 3D printer and Application will allow the uploading, controlling, and initiation of printing from anywhere with internet access
  Quicker Z-axis motion
  Print time within 10% of a regular Ender 3 Printer

## Slide 3: System Overview

## Slide 4: Task Partition
Abigail: Program ESP32-S3
Cody: Design power distribution board, stepper motor, hotend, and heated bed controllers
Steven: Design and program the application and web hosted server

## Slide 5: Electrical System Overview

## Slide 6: Electrical System Overview
Power Distribution
  Split 24V 15A into four 5V 1A outputs, a 5V 0.5A output, a 24V 9.167A output, and a 24V 1.67A output
Stepper Motor Drivers
  Design 4 stepper motors drivers to control
  Three at 5V 0.84A and one at 5V 1A
Hotend
  N-Type MOSFET that takes MCU inputs and allows 24V 9.167A through
Heated Bed
  N-Type MOSFET that takes MCU inputs and allows 24V 1.67A through

## Slide 7: Microcontroller Unit
ESP32-S3
Connects all subsystems
Communicates to server
Controls all printer components

## Slide 8: MCU Coding
Programmed in C
Reads in user input and files from application
Translates G-code to printer
Controls heating elements and stepper motors
Drives extruder
Links device to the internet

## Slide 9: Phone Application
Perform all the tasks of the original software
Developed in Android Studio using Kotlin Programming Language
Start Print
Select Print
Printer Status:
Server Status:
Printer Name
Bed Temperature 0°
Extruder Temperature 0°
Extruder Position 0.0.0
Fan Speed 0
Last updated: 0s

## Slide 10: Server
Intercommunication between mobile application and physical printer
Stores a library of previous prints

## Slide 11: User Interface Model
Printing
18%
model_bridge
Printer Status:
Server Status:
Printer Name
Bed Temperature 0°
Extruder Temperature 0°
Extruder Position 0.0.0
Fan Speed 0
Last updated: 0s
Start Print
Select Print
Printer Status:
Server Status:
Printer Settings
Print Library
Printer Name
Settings
Bed Temperature 0°
Extruder Temperature 0°
Extruder Position 0.0.0
Last updated: 0s
Printer Settings
Bed Temperature
Extruder Temperature
Home Position
Revert
Print Library
Print
Upload Print to Library
Select Print File
Search Library
model_ship
model_plane
Skeleton_hand
mini_whale
Print Library
Print
Upload Print to Library
Select Print File
Search Library
model_ship
model_plane
Skeleton_hand
mini_whale
Select Print File
Select from Library
Select from Files

## Slide 12: Execution Plan

## Slide 13: Validation Plan